## Slide 1: CODING A SPIRIT LEVEL
Page:
Kitronik | LESSON PLANS
WITH THE ZIP HALO

## Slide 2: A SPIRIT LEVEL
Page:
Kitronik | LESSON PLANS

## Slide 3: Accelerometer orientation
Page:
Kitronik | LESSON PLANS

## Slide 4: Initial ALgoRiTHM
Page:
Kitronik | LESSON PLANS
IF micro:bit is not level THEN
Display red

## Slide 5: Improved ALGORITHm
Page:
Kitronik | LESSON PLANS
FOREVER
IF acceleration(x) < XLevel THEN
Display red
ELSE IF acceleration(x) > Xlevel THEN
Display red
ELSE IF acceleration(y) < YLevel THEN
Display red
ELSE IF acceleration(y) > Ylevel THEN
Display red

## Slide 6: Algorithm for reduced sensitivity
Page:
Kitronik | LESSON PLANS
FOREVER
IF acceleration(x) < XLevel - 5 THEN
Display red
ELSE IF acceleration(x) > Xlevel + 5 THEN
Display red
ELSE IF acceleration(y) < YLeve l - 5 THEN
Display red
ELSE IF acceleration(y) > Ylevel + 5 THEN
Display red

## Slide 7: PATTERN SPOTTING
Page:
Kitronik | LESSON PLANS
FOREVER
IF acceleration(x) < Xlevel - 5 OR
acceleration(x) > Xlevel +5 THEN
Display red
ELSE IF acceleration(y) < Ylevel - 5 OR
acceleration(y) > Ylevel + 5 THEN
Display red

## Slide 8: Final algorithm
Page:
Kitronik | LESSON PLANS
Show red
FOREVER
IF acceleration(x) < XLevel -5 THEN
Display
ELSE IF acceleration(x) > Xlevel + 5 THEN
Display
ELSE IF acceleration(y) < Ylevel - 5 THEN
Display
ELSE IF acceleration(y) > Ylevel + 5 THEN
Display
ELSE
Display green

## Slide 9: SETUP
Page:
Kitronik | LESSON PLANS
1. Under Variables select “Make a Variable” and give it a name, e.g. Halo
          2. Under NeoPixel drag out “Set strip to Neopixel at pin P0 with 24 leds as RGB (GRB format)” and add it under “on start”
a. Change ‘strip’ to Halo
          b. Notice how it’s connected to P0 – this is correct
c. Notice how it’s 24 LEDS – this is correct. If we had more LEDs we’d change this number.
d. Our lights are also in the RGB (GRB format).

## Slide 10: SAVE YOUR EYES!
Page:
Kitronik | LESSON PLANS
Neopixel > More
Item set brightness 255
Change item to Halo
Change 255 to 10

## Slide 11: Challenge 1 - Get your data
Page:
Kitronik | LESSON PLANS
On A Button Press
While True
Show number: acceleration(x)
On B Button Press
While True
Show number: acceleration(y)
WHAT IS LEVEL?

## Slide 12: Challenge 1 - Get your data
Page:
Kitronik | LESSON PLANS
On A Button Press
While True
Show number: acceleration(x)
On B Button Press
While True
Show number: acceleration(y)
WHAT IS LEVEL?

## Slide 13: Setup
Page:
Kitronik | LESSON PLANS

## Slide 14: CODE
Page:
Kitronik | LESSON PLANS

## Slide 15: ALGoRiTHM
Page:
Kitronik | LESSON PLANS
If acceleration(x) > XLevel THEN
Turn on lights 16, 17, 18, 19, 20

## Slide 16: ALGoRiTHM
Page:
Kitronik | LESSON PLANS
IF acceleration(x) < XLevel THEN
Turn on lights 4, 5, 6, 7, 8

## Slide 17: HALO ALGoRiTHM
Page:
Kitronik | LESSON PLANS
FOREVER
IF acceleration(x) > XLevel-50 THEN
Display
Turn on lights 17, 18, 19, 20, 21
ELSE IF acceleration(x) < Xlevel+50 THEN
Display
Turn on lights 5, 6, 7, 8, 9
ELSE IF acceleration(y) > YLevel-50 THEN
Display
Turn on lights 23, 24, 1, 2, 3
ELSE IF acceleration(y) < Ylevel+50 THEN
Display
Turn on lights 11, 12, 13, 14, 15
ELSE
Display green

## Slide 18: CODE
Page:
Kitronik | LESSON PLANS

## Slide 19: CODE
Page:
Kitronik | LESSON PLANS